## Slide 1: RDCH 702 Lecture 7: Radiation Reactions: Dosimetry and Hot Atom Chemistry
Readings:
  Reading: Modern Nuclear Chemistry, Chap. 17; Nuclear and Radiochemistry, Chap. 6, Chap 11.C.
Interaction of radiation with matter
  Neutron, positive ions, electrons, photons
Dosimetry
Radiation Protection
Hot Atom Chemistry
Effect in biological systems
Radicals are formed by the interaction of radiation with water
  Radicals drive reactions

## Slide 2: Interaction of Radiation with Matter
Interaction of radiation with matter leads to:
  dissociation of molecules
  excitation of atoms or molecules
  ionization of atoms or molecules
Ionization is easily measured
  used for detection
In air about 35 eV of energy are dissipated for each ion pair formed
Other gases
Xe: 21.9 eV, He: 43 eV, NH3: 39 eV (IP = 10.8 eV), Ge: 2.9 eV
  Radiation detected by interaction with matter
  Interactions ultimately have the same effect
    (35 ev/ion pair formation)
  Measure total number of ions produced to determine energy
Energy Loss Overview
At sufficiently high energy ion is bare and energy loss is through electronic excitation and ionization of stopping material
At velocities comparable to the K-shell electron, ion begins to pick up electrons, stopping is still electronic
At velocities comparable to valence electrons elastic collisions account for energy loss
  nuclear stopping
No sharp difference point between methods 2 and 3
  elastic and inelastic collisions

## Slide 3: Positive Ions
Processes for energy loss
  Chiefly by interactions with electrons
Maximum velocity (v) imparted to electron is 2v
  KE =0.5mv2; v =(KE/0.5m)2
    Consider maximum energy from 6 MeV alpha to electron
    Average energy from ions to electrons is 100-200 eV
      Secondary ionization
Electronic stopping
  inelastic collisions between bound electrons and ion
    Excitation of atomic electrons
Nuclear stopping
  velocity of ion close to velocity of valence electrons
  elastic collisions dominate
Velocity of the ion comparable to K shell electron, ion begins to pick up electrons
  Ions passing through matter
    stripped of all orbital electrons whose orbital velocity is less than ion velocity
Interaction with matter
Neutrons
  Very little interaction with electron, primary ionization is negligible
  Interaction confined to nuclear effect
    scattering (elastic and inelastic)
    reactions (n,), (n,p), (n,), (n,2n)
    fission

## Slide 4: Range
Due to large mass of positive ion compared to electron
distances that positive ions travel in matter are in narrow limits
  Particle and energy dependent
  Defined as range
Large mass drives behavior
  Fractional energy loss per collision is small
    large number of collisions required to stop ion
  Deflection of ion in each collision is small
Straggling is fluctuations in average energy loss and projected path
  order of a few percent
Number of ions from a point source fn(distance)

## Slide 5: Electrons
Energy loss
  similar to that of positive ions
  average ion pair formation about 35 eV in air
  70-80% of ionization is secondary
Electron has less mass than positive ions
  For the same energy, higher velocity
  Lower stopping power
Maximum at 146 eV (5950 ion pairs per mg/cm2)
In air ionization stops around 12.5 eV
Electron can lose a large fraction of energy in one collision
Straggling is more pronounced
Energy loss through electron interaction, nuclear scattering

## Slide 6: Electron Backscattering
Significant fraction of electrons may be reflected from scattering
Reflected intensity increases with increasing thickness of reflector
  Saturation can be achieved
Ratio of measured activity beta source with reflector to that without reflector is back-scattering factor
Factor varies with material
  Used to determine Z of material

## Slide 7: Photons
Lose most energy in a few interaction or a single interaction
Need more material for interaction than electron
Average specific ionization is less than electron (10%)
Average energy loss per ion pair formation in air is 35 eV
Photoelectric effect
photon with energy hv ejects bound electron and imparts energy hv-b to electron
  b is electron binding energy
Mostly K-shell, some L-shell (about 20%)
Proportional to Z5 of absorber
For 5% photoelectric effect,  energy needed for different Z
  Al- 0.15 MeV
  Cu-0.4 MeV
  Sn-1.2 MeV
  Pb-4.7 MeV

## Slide 8: Compton Effect
Photon loss part of energy to electron
Photon is scattered
Minimum for scattered photon is
Eo= electron rest energy
Back scattering peak can be seen on spectra
Pair Production
Production of ß+ and ß-
Proportional to energy (log E about 4 MeV) and Z2
More common at high energy
511 keV from positron-electron annihilation

## Slide 9
Energy Dependence
Effects with different materials
Al
Cu
Pb

## Slide 10: Radiation Dose Units
Absorbed Dose
  energy absorbed per unit mass of target for any kind of ionizing energy
  Gray (Gy) = 1J/kg
  in US; rad = 100 erg/g
  1J/kg = 107 erg/103 g = 104 erg/g
    100 rad=1 Gy
Absorbed dose is referred to as dose
Treated as point function, having a value at every position in an irradiated object
1 eV = 1.60E-19 J
1 charge pair separation =1.60E-19 C
Radicals are formed by the interaction of radiation with water
  Radicals drive reactions
Dosimetry
Quantitative relation between specific measurement in a radiation field and chemical and/or biological changes
  dose effect relationship
  caused by production of ionized molecules, atoms, secondary electrons
  chemical changes, biological effects

## Slide 11: Dose Equivalent
Absorbed dose needed to achieve biological effect is different for different types of radiation
  Difference due to high versus low linear energy transfer (LET)
  Dose equivalent compensates for this difference
  H (dose equivalent) = QD
  Q is dimensionless, has some different values
  Q=fn(particle, energy); 1≤Q≤20
    Q from NCRP Report 116
  uses LET (L) in keV/µm in water
Radiation QF
X and grays 1
Electrons and Positrons 1
Neutrons, E < 10 keV 3
Neutrons, E > 10 keV 10
Protons 1-10
Alpha Particles 1-20
Heavy Ions 20
Q Dependence on LET
LET (L) Q
(kev/µm in water)
<10 1
10-100 0.32L-2.2
>100 300/L^0.5

## Slide 12: Dose Equivalent
When dose in Gy, dose equivalent is Sv
When dose in rad, dose equivalent is rem (roentgen-equivalent-man)
1 Gy = 100 rad, 1 Sv = 100 rem
Particle type and energy should be explicitly considered
Biological distribution can depend on isotope
  I to thyroid
  Sr, Ra to bone
  Cs, H widely distributed
  Metals go towards liver
  Complexes can be released in kidneys
    pH change

## Slide 13: Radiation Protection
6.24 mSv/y Typical background radiation to US public
  Value updated
2.4 mSv/y Average dose to US nuclear industry employees. (0.01mSv/y to public)
350 mSv in lifetime Criterion for relocating people after Chernobyl
50 mSv annual worker dose limit
15 µSv to public from Three Mile Island in 50 mile radius
0.4 mSv from dental x-rays
1000 mSv as short term dose: causes (temporary) radiation sickness.
5000 mSv as short term dose: would kill about half those receiving it within a month.
10,000 mSv as short term dose: fatal within days

## Slide 14: Dose Calculations
Alpha and Beta
Absorbed dose: D = AEavex1.6E-13J/MeVx1E3g/kg
=1.6E-10AEave (Gy/s)
A = conc. Bq/g,
Eave= average energy
Calculated dose of 1.2 E5 Bq of 14C in 50 g of tissue
ßmax of 14C is 0.156 MeV
Eave≈ ßmax/3 ≈ 0.052 MeV
A = 1.2 E5 Bq/50g
D = 1.2 E5 Bq/50g x 0.052 MeV x 1.6E-10 = 20 nGy/s
What does this value mean?
Average background 6.24 mSv/year
2E-10 Sv/second= 0.2 nSv/s

## Slide 15: More Dose Calculations
Photons
µ/r is air energy absorption coefficient
= 0.0027 m2/kg for 60 keV to 2 MeV
D = 3.44E-17 CE/r2 (Gy/s)
C in Bq, E in MeV and r, distance from source, in m
gamma energy needs to normalized to %
Dose from 10000 Bq 38S at 0.1 m
95 % gamma yield 1.88 MeV
D= 3.44E-17 x 1E5 x 1.88*0.95 / 0.12
D = 6.14E-10 Gy/s
Need to consider average gamma energy

## Slide 16: Probability Coefficients for Stochastic Effects
Detriment Adult Workers Whole Pop.
(1E-2/Sv) (1E-2/Sv)
Fatal Cancer 4.0 5.0
Nonfatal Cancer 0.8 1.0
Severe genetic
effects 0.8 1.3
TOTAL 5.6 7.3
What is probability of detriment from 2 mSv/y for 10 years to adult worker?
2E-3 Sv/y x 5.6E-2/Sv x 10 y = 1.1E-3
From maximum occupation dose for 30 years
50E-3 Sv/y x 5.6E-2/Sv x 30 y = 0.084

## Slide 17: Biological Effects Concepts
Linear Effect of Dose
  Any amount radiation above background is harmful
  Basis of radioisotope exposure limits
  http://www.nrc.gov/reading-rm/doc-collections/cfr/part020/
  Low level radiation effect not so clear

## Slide 18: Intake limits
Air and water
  nuclide specific (include daughter)
  Class refers to lung retention (Days, Weeks, Years)
  Annual limits on Intake (ALI) derived from 0.05 Sv total dose or 0.5 Sv dose to an organ or tissue
  Derived air concentration (DAC) comes from ALI
  DAC = ALI/(2000 hr x 60 min/hr x 2E4 mL/min)
Atomic No. | Radio-nuclide | Class | Table 1 Occupational Values |  |  | Table 2 Effluent Concentrations |  | Table 3 Releases to Sewers
 |  |  | Col. 1 | Col. 2 | Col. 3 | Col. 1 | Col. 2 | 
 |  |  | Oral Ingestion ALI (µCi) | Inhalation |  | Air (µCi/ml) | Water (µCi/ml) | Monthly Average Concentration (µCi/ml)
 |  |  |  | ALI (µCi) | DAC (µCi/ml) |  |  | 
95 | Am-241 | W, all compounds | 8E-1 Bone Surf | 6E-3 Bone Surf | 3E-12 | - | - | -
 |  |  | (1E+0) | (1E-2) | - | 2E-14 | 2E-8 | 2E-7
Isotope data found at: http://www.nrc.gov/reading-rm/doc-collections/cfr/part020/appb

## Slide 19: Laboratory usage
ALI and DAC basis of activities levels in the laboratory
  http://rms.unlv.edu/radiological/Form%202%20-%20Risk%20Assessment%20and%20Control%20Guideline%20for%20RAM%20(2).pdf
Use data to correlate isotope mass, experimental method, and activity level

## Slide 23: Level calculations
Level 2 for 238U, non-airborne
  Up to 1 ALI-ingestions
    10 mCi limit
  A=3.7E5 Bq, l= 4.88E-18 s-1
  A/ l=N, N=7.58E22=0.126 moles=30 g U
    Level 3, non-airborne 500 mCi limit
    1500 g U, in fume hood
Level 3 for for 99Tc, non-airborne
  Up to 50000 mCi limit
  A=1.85E9 Bq, l= 1.03E-13 s-1
  A/ l=N, N=1.79E22=2.98E-2 moles=2.95 g Tc

## Slide 24: Hot Atom Chemistry
Chemical processes that occur during nuclear reactions
  Also called Szilard-Chalmers process
Example: Activity of I extracted from water and ethyl iodide
  Precipitated at AgI
Chemical reactions produced by nuclear transformation
  Neutron irradiation of ethyl iodide
    Iodine extracted into aqueous phase
      127I(n,g)128I
        Possible to produce specific isotope
Need to overcome bond energy
  Neutron does not normally contain sufficient energy
  Gamma decay can provide suitable energy from recoil
    M is atom mass, E is gamma energy in MeV
      Nucleus excited 6-8 MeV

## Slide 25: Hot Atom Chemistry
Bonds are broken due to reaction energy
  Bond energies on the order of eV
Conditions needed
  Bond of produced atom must be broken
  Should not recombine with fragments
  Should not exchange with target molecule
    Slow kinetics
  Separation of new species
Halogens produced in this method
  CCl4
  C2H2Cl2
  C2H5Br
  C2H2Br2
  C6H5Br
  CH3 I
    Used to produce 38Cl, 80Br, 82Br, 128I

## Slide 26: Hot Atom Chemistry: Chemical Reactions
Beta reactions can also be exploited
  TeO32-IO3- + e-
    Recoil is not quantized
      Kinetic energy shared
      E is maximum beta energy (MeV)
        Rmax(eV)=573E(E+1.02)/M
        0.5 MeV in 100 amu is about 4 MeV
      Energy is distributed
        Translational, rotational, vibrational
      Bond usually not broken
  Internal conversion set atom in excited state
    Rearrangement of electrons and drive chemical reactions
    Separation of isomers

## Slide 27: Review
Interaction of radiation with matter
Dosimetry
  Calculations
  Units
  limitation
  Influence of particles
  Measurements
Hot Atom Chemistry
  Energetic processes

## Slide 28: Questions
Compare DAC for isotopes of Pu and Cs
Perform a dose calculation for 1 mg internal exposure of 210Po
Use DAC to evaluate experimental limits for 241Am
Calculate the dose from 500000 Bq of 241Am at 0.050 m
What are the different masses of 99Tc permitted for the various laboratory safety levels at UNLV.
What are the principles of hot atom chemistry

## Slide 29: Questions
Comment on the blog
Respond to PDF Quiz 7