## Slide 1: RDCH 702 Lecture 11 Part 1 Applications of nuclear material
Readings: Nuclear and Radiochemistry Chapter 11.D
Modern Nuclear Chemistry Chapter 4.10
Outline
Isotope production methods
Neutron generators
Ionization sources
Heat source
Radiopharmaceuticals
  Diagnostic
    Gamma emission
      Positron emission tomography
  Therapeutic
    Auger electron, Beta Decay, Alpha Decay

## Slide 2: Isotope production: Fission
Fission
  Direct production of fission products
  Neutron reactions to form actinides
  238U+n239U239Np+b- 239Pu+b-
    Can go up to 252Cf
Production of radioisotopes
  Fission products
  Neutrons for neutron capture
    238Pu: 237Np(n,g)
    241Am
      Neutron capture on Pu isotopes, beta decay of 241Pu

## Slide 3: Fission Products
Fission yield curve varies with fissile isotope
  Elements Se (Z=34) to Dy (Z=66)
2 peak areas for U and Pu thermal neutron induced fission
Variation in light fragment peak
  Higher peak stable due to magic numbers
Influence of neutron energy observed
Neutron rich isotopes, beta decay
235U fission yield

## Slide 4: Accelerator production
Charged particle at high energy
  Nuclear interactions between projectile and target
Can vary target, projectile, separations
  Amount of material
  Energy
Production of neutron poor isotopes
  Positron emitters

## Slide 5: Neutron emitters
Determine elements in samples based on reactions with neutrons
  Na, Actinides
Evaluation of subcritical amounts of fissile material
Detect water or hydrogen by backscattering
Explosives
  utilizes cross-section resonances of N and O
    Explosives have characteristic N to O ratios
      Measurement of characteristic gammas from reaction or absorption of neutrons

## Slide 6: Neutron emitters
252Cf as neutron source
Reaction of alpha particle on Be
  9Be(a,n)12C
  Can use different alpha source
    241Am
    239,240Pu
    210Po

## Slide 7: Emitted Particle Interaction
Smoke detectors
  241Am alpha emission
  AmO2, 33 kBq of 241Am
  Smoke detection by ionization chamber
    Alpha particles ionize air
      Ions detection through low level current in ionization chamber
    Smoke enters chamber between electrodes, drop in ion formation
      Ions will attach to smoke particles
    Decrease in electric current triggers alarm

## Slide 8: Emitted particle interaction
Explosive detection
  63Ni beta emission
  Ion mobility detector
    Sample collected
      can determine pgram level
    Molecules ionized by beta particles
      Cross section related to ion size and shape
    Migration of molecules in chamber based on mass, size and shape
      Chamber filled with gas
      Detector at end
      Migration time characteristic for ion

## Slide 9: 238Pu properties
Half-life 87.7 a
237Np(n,g)238Np
  238Pu from beta decay of 238Np (t1/2=2.12 d)
  Separated from unreacted Np by ion exchange
Decay of 242Cm
0.57 W/g
Power source for space exploration
  83.5 % 238Pu, chemical form as dioxide
  Enriched 16O to limit neutron emission
    6000 n s-1g-1
    0.418 W/g PuO2
150 g PuO2 in Ir-0.3 % W container

## Slide 10: 238Pu production
238Pu prepared at Savannah River by irradiating NpO2 particles embedded in an aluminum matrix
Anion exchange in nitric acid solution was used to separate the Np and Pu from the fission products
  Then separate Pu from Np
Irradiated aluminum targets dissolved in 10 M nitric acid containing small amounts of KF and mercuric nitrate
  nitric acid solution was treated to give a nitric acid concentration of 8 M and ferrous sulfamate was used to adjust the valence of Np and Pu to the tetravalent state
A first stage of anion exchange on a Dowex I type resin separated the Np(IV) and Pu(IV) (held on the resin as anionic nitrato complexes) from the aluminum and the bulk of the fission products
In the second stage of anion exchange, Pu(IV) and Np(IV) were again bound to the column and the Pu selectively eluted as Pu(III) using 5.5 M nitric acid 0.05 M ferrous sulfamate and 0.05 M hydrazine.
Np(IV) was eluted from the second column with 0.35 M nitric acid, precipitated as the oxalate complex, and then calcined to NpO2 for reuse in new targets
238Pu was purified in a third stage of anion exchange and the eluted 238Pu nitrate solution sent on for further processing into PuO2 or other compounds
General Purpose
Heat Source - GPHS
Iridium-clad capsule
Equatorial tungsten
arc weld
62.5 Watt: 152g 238PuO2

## Slide 11
Planetary Exploration – Heat for Mars Rovers
8 LWRHUs
2.7g 238PuO2 1 Watt
Twin Rovers

## Slide 12
Radioisotope Thermoelectric Generator
2 GPHS pellets per impact shell
2 impact shells per module
18 modules per RTG
Total 72 GPHS pellets per RTG
11 kg Pu
200 Watts power

## Slide 13
Cassini Heat and Power Sources
333 LANL Heat Sources
117 RHUs (0.3 kg)
  heat for spacecraft components
216 GPHS pellets (32 kg)
  electrical power

## Slide 14
New Horizons Pluto-Kuiper Belt Mission
61 GPHS pellets
1 RTG, 170 Watts
10 kg plutonium
Arrival 2015

## Slide 15: RDCH 702 Lecture 11 Part 1 Applications of nuclear material
Readings: Nuclear and Radiochemistry Chapter 11.D
Modern Nuclear Chemistry Chapter 4.10
Outline
Isotope production methods
Neutron generators
Ionization sources
Heat source
Radiopharmaceuticals
  Diagnostic
    Gamma emission
      Positron emission tomography
  Therapeutic
    Auger electron, Beta Decay, Alpha Decay